M & M SALES, INC.

------------------------   Manufacturer’s Representative  ------------------------

MAIN OFFICE: 3415 VASSAR NE  ALBUQUERQUE, NM 87107  PHONE: (505) 884-1733 FAX: (505) 888-4896

EL PASO OFFICE: 1006-B WALL ST. EL PASO, TX 79915 PHONE (915) 772-0393 FAX: (915) 772-0683

Gas Pressure Regulators

The following questions must be answered to properly size a gas regulator:

1 – What is the inlet gas pressure?

2 – What is the desired outlet gas pressure?

3 – What volume of gas is required through the regulator? (CFH)

(May be expressed in BTU’s required)

4 – What type of gas? (Natural Gas or LP Gas)

5 – Will the regulator be mounted inside or outside the building? If inside, will the

regulator be vented to the outside or will it require a vent limiting device?

Helpful Information

Gas Pressure –

Gas pressure is expressed in terms of pounds, ounces, or inches of water column.

1 psi  = 16 ozs. = 28” w.c.

.50 psi = 8 ozs. = 14” w.c.

.25 psi = 4 ozs. = 7”   w.c.

Gas Volume –

Gas flow rate is measured in Cubic Feet per Hour (CFH)

Equivalents –

For Natural Gas: There are approx. 1000 BTU’s per Cubic Foot

For LP Gas: There are approx. 2500 BTU’s per Cubic Foot

MBH = 1000 btu’s per hour (Ex. 3000 MBH = 3,000,000 btu’s/hr)

LP gas –

Capacity charts for Natural Gas should be factored x.63 to get LP gas capacities.